## Slide 1: EECE3264 Lab06 StateChart
TIMER0 overflow interrupt (1mS)
Reset TIMER0 overflow counter
Return from interrupt
Tick = Tick + 1
Tick = 50?
Start main program
Turn on and off LED(s) given the current Mode
Tick = 0
Y
N
Initialize interrupts
Mode = 0; Tick = 0
NB: This process also sets a “modeChanged” flag, which is sensed and cleared by main.
Switch
interrupt
Mode = 0?
Mode = 1
Mode = 1?
Mode = 2
Mode = 2?
Mode = 3
Mode = 0
Return from interrupt
N
N
N
Y
Y
Y
The main loop reads Mode and Tick
(and sometimes resets Tick to zero)
The Switch interrupt code changes Mode
The TIMER0 code increments
Tick once every millisecond

## Slide 2: EECE3264 Lab06 StateChart
TIMER0 overflow interrupt (1mS)
Reset TIMER0 overflow counter
Return from interrupt
Tick = Tick + 1
Tick = 50?
Start main program
Turn on and off LED(s) given the current Mode
Tick = 0
Y
N
Initialize interrupts
Mode = 0; Tick = 0
NB: This process also sets a “modeChanged” flag, which is sensed and cleared by main.
Switch
interrupt
Mode = 0?
Mode = 1
Mode = 1?
Mode = 2
Mode = 2?
Mode = 3
Mode = 0
Return from interrupt
N
N
N
Y
Y
Y
The main loop reads Mode and Tick
(and sometimes resets Tick to zero)
The Switch interrupt code changes Mode
The TIMER0 code increments
Tick once every millisecond

## Slide 3: Handling Interrupts in C
AVR Studio provides good support for interrupt processing in C
  ISR handler must be named “ISR”
  Argument must be a specific interrupt vector name as defined in the iom128a.h file
  iom128a.h also defines register names and bit operators, too—very helpful!
Tip: While programming, R-click on a defined constant, macro, variable, or function name and choose “Goto Implementation”—Atmel Studio will find and open the source definition for you!
ISR(INT1_vect)
{
...
}

## Slide 4: A State-Driven Interrupt Handler Framework (1 of 3)
#include <avr/io.h> // standard AVR header
#include <avr/interrupt.h> // needed for interrupts
#include <avr/delay.h> // needed to use _delay_ms()
#define DELAY 50
// enumerate the possible patterns
enum patterns
{
RightToLeft, // E0 to E7
LeftToRight, // E7 to E0
BackAndForth, // E0 to E7 to E0
MysteryPattern // ???
};
// global variable to keep track of the current LED pattern
enum patterns Mode;
int main(void)
{
...
NB: You’re not allowed to use _delay_ms() in Lab06!! (Use a tick-timer instead)

## Slide 5: A State-Driven Interrupt Handler Framework (2 of 3)
int main(void)
{
// declare variables, initialize HW registers (interrupts,
// ports, etc.) and initialize Mode to starting pattern
// enable interrupts globally
sei();
while(1) // loop forever
{
// execute code based on the current pattern
switch(Mode)
{
case(RightToLeft):
// turn off current LED, turn on next LED in the pattern
break;
case(LeftToRight):
}
_delay_ms(DELAY); // leave the LED on for 50mS
}
}
Again, don’t use _delay_ms() in Lab06. Instead, wait here until “Tick” reaches 50 (incremented automatically via the timer ISR).
Once it reaches 50, reset it to zero and continue looping.
Switch-Case statements are more compact than if-then-else statements
…

## Slide 6: A State-Driven Interrupt Handler Framework (3 of 3)
ISR(INTxx_vect)
{
// Invoked when joystick button PB4 (which must be connected
// externally to a pin that can cause interrupts) is released
// change LED blinking pattern
switch(Mode)
{
case(RightToLeft):
Mode = LeftToRight;
break;
case(LeftToRight):
Mode = BackAndForth;
break;
}
}
NB: This is NOT the correct interrupt number for Lab06!
…